## Slide 1: DIP-CSE-4205 Chapter-3 Intensity Transformation and Spatial Filtering
Department of Computer Science and Engineering
Comilla University, Cumilla

## Slide 2
Piecewise-linear transformation functions are functions defined by different linear expressions, each applying to a specific interval of the input domain.
These functions are "piecewise" because they are constructed from multiple linear pieces, each applying to a specific subdomain.
They are commonly used in various fields, including image processing, optimization, and control systems.
Piecewise-Linear Transformation Function

## Slide 3
Piecewise-Linear Transformation Function

## Slide 4
Image Processing: Contrast Stretching, intensity-level slicing.
Control Systems: Approximating nonlinear controllers.
Machine Learning: Activation functions (e.g., ReLU is a simple piecewise-linear function).
Mathematics: Approximating non-linear curves with linear segments.
Application

## Slide 5
Contrast stretching is an image enhancement technique that
Enhance the contrast of an image by expanding the range of intensity values.
Remapping the original intensity values to a wider or more desirable range using a piecewise-linear transformation function.
Contrast Stretching

## Slide 6
Low-contrast images (e.g., underexposed or foggy images) have pixel values clustered in a narrow range
- If an image has intensity values in a narrow range (e.g., 50–150), contrast stretching maps them to a wider range (e.g., 0–255).
Why Use Contrast Stretching?

## Slide 7
Formula:
Contrast Stretching

## Slide 8
Medical Imaging: Enhancing X-rays/MRI scans.
Surveillance: Improving visibility in low-light conditions.
Satellite Imagery: Adjusting land/water contrast.
Application (Contrast Stretching)

## Slide 9
Intensity-Level Slicing is an image enhancement technique that
Highlight specific ranges of intensity values in an image while suppressing others
Instead of enhancing the entire dynamic range like contrast stretching, it focuses on emphasizing certain pixel intensities
Useful for feature extraction, enhancing regions of interest (ROI), and medical imaging (e.g., isolating tumors or blood vessels).
Intensity-Level Slicing

## Slide 10
Binary Slicing (Highlighting)/ Without Background Preservation
Only the specified intensity range is highlighted, and all other pixels are suppressed (set to black or zero).
Formula:
Types of Intensity-Level Slicing

## Slide 11
2. Background-Preserving Slicing / With Background Preservation
The specified intensity range is highlighted, but all other intensities are retained as they are.
Formula:
Types of Intensity-Level Slicing

## Slide 12
In a grayscale image, highlight bones or tissues that fall within an intensity range of 100–150:
Intensities between 100–150 → set to white (255)
Others → set to 0 (black) or remain unchanged
Use Case Example

## Slide 13
Medical Imaging: Isolating bone structures in X-rays.
Industrial Inspection: Detecting defects in materials.
Astronomy: Highlighting celestial objects.
Application

## Slide 14
Histogram
- represents the frequency distribution of pixel intensity values in an image
Histogram Processing
- analyzing and manipulating the histogram of an image to enhance its visual quality or extract specific features
- enhancing contrast, improving brightness, and performing image equalization
Histogram processing

## Slide 15
Histogram Equalization:
    Redistribute pixel intensities to achieve a uniform histogram
    Improve global contrast of the image
    Enhances the overall visibility of features, especially in images with poor contrast
If most pixels are in the dark range, equalization will stretch and shift them to cover a wider range, brightening the image
Histogram processing Techniques

## Slide 16
Steps:
Compute the histogram of the original image.
Calculate the cumulative distribution function (CDF).
Map intensities using the CDF.
Round the values to the nearest integer.
Histogram Equalization
Where,
nj= number of pixels that have intensity rk
N= Total number of pixels

## Slide 17
2. Histogram Matching (Specification):
    Modify the histogram of an image to match a desired histogram (e.g., a reference image)
    Useful for normalizing images in medical imaging or matching lighting conditions
Histogram processing Techniques

## Slide 18
Steps:
Compute the histogram of the input image and its CDF
Compute the CDF of the desired histogram
For each intensity level in the input image, find the closest intensity in the desired CDF.
Remap the pixel values accordingly.
Histogram Matching (Specification)

## Slide 19
-A fundamental technique in digital image processing used to modify or enhance an image by applying a mathematical operation over a neighborhood of pixels.
-Applied directly to an image in the spatial domain—that is, pixel by pixel
-Used for tasks like smoothing (blurring), sharpening, edge detection, and noise reduction
Spatial Filtering

## Slide 20
A filter or kernel (a small rectangular region e.g., 3x3, 5x5) is placed over a pixel and its neighborhood.
Each pixel in the neighborhood is multiplied by the corresponding kernel value.
The results are summed (and sometimes normalized) to produce the new value for the center pixel.
This process is repeated for every pixel in the image (convolution).
How It Works

## Slide 21
For a 3x3 kernel applied to a pixel at position (x, y):
Kernel:
Neighborhood pixel values:
New pixel value = k1*p1 + k2*p2 + k3*p3 + k4*p4 + k5*p5 + k6*p6 + k7*p7 + k8*p8 + k9*p9
How It Works (Example)

## Slide 22
Spatial filters are broadly categorized into two types:
a. Linear Filters
The output is a weighted sum of input pixel values.
Common examples:
1. Smoothing (Low-Pass) Filters: Reduce noise and blur the image.
Example: Mean filter (averages neighborhood pixels).
Types of Spatial Filters

## Slide 23
2. Sharpening (High-Pass) Filters: Enhance edges and details.
Example: Laplacian filter (emphasizes edges).
3. Edge Detection Filters: Highlight edges.
Example: Sobel filter (detects horizontal or vertical edges).
Types of Spatial Filters

## Slide 24
b. Non-Linear Filters
The output is not a simple weighted sum but depends on a non-linear operation.
Common examples:
1. Median Filter: Replaces the center pixel with the median value of the neighborhood. Effective for removing salt-and-pepper noise.
2. Min/Max Filters: Replace the center pixel with the minimum or maximum value in the neighborhood.
3. Rank-Order Filters: Sort neighborhood pixels and select a specific rank.
Types of Spatial Filters